Automated calibration for CALIFA
Mrunmoy Jena
CALIFA WG Meeting
18.10.24
Calibration in the gamma range
Extrapolation to proton range
Gain matching
Supported by BMBF 05P15WOFNA and 05P19WOFN1
Physics with R3B
CALIFA – Design
TUM Members:
Roman Gernhäuser,Philipp Klenze,Tobias Jenegger, Mrunmoy Jena

---
Gamma range: uncalibrated spectra
Back barrel
iPhos
CEPA
Barrel
Starting point: gain matched channels from s118, not perfect
Calibration macro: peak finding, Gaussian fits, linear fit to source + 3 pulsers

---
Gamma range: calibrated spectra
Source peak is calibrated, but odd-even staggering in pulser peaks
Need to calibrate coupling capacitors, for each channel !

---
Thank you!
Coupling capacitors inside
Rc
Gain resistors “switch”
Cp
C1/C2
Pulser in

---
Proton range: uncalibrated spectra

---
Proton range: calibrated spectra
Similar procedure adpoted, fits made with 6 pulsers
Calibration works in practice, still need for calibrating the coupling capacitors

---
~6 per mil. Tolerance
Variation in the capacities of the coupling capacitors effectively cancels out
Calibration can now be extended to full range
Next step: similar speed up for gain matching
R=Eγ/Ep = [(Q/C)γ]/[(Q/C)p] ≈ 11

---
Summary
LMD files (90 GB) to unpacked .root files (60 GB): takes 4.2 hrs
Unpacked .root files to spectrum.root (60 MB): 40 mins
Spectra written to calibrated.root (36 MB): only a few mins !
Calibration parameters written to a file
Rather small spectrum file, written only once for the entire procedure
Advantages: automation, peak finding proceeds quickly